## Slide 1
NETHEAL / NC-04
Self-healing campus network
Detection, root cause analysis and evaluation
01
Observe → detect → diagnose → decide
Heal → verify → explain
15 devices · 27 links · 9 traffic demands
Notes: Opening, 20 seconds: A redundant campus can still deliver poor service when its current routes cross a failed or overloaded component. NetHeal observes telemetry, detects the problem, diagnoses supported causes, chooses a permitted mitigation and measures recovery. The demonstration uses a simulated campus. The LLM explains evidence and writes incident reports.
Sources: supplied NC-04 problem statement, config/campus.yaml, services/gateway/main.py and docs/LIMITATIONS.md.

## Slide 2
NETHEAL / NC-04
Detection
Telemetry becomes a current, evidence-backed alert
02
1 Validate and learn
Latency, loss and load; a trusted healthy baseline
2 Find unhealthy service
Robust z + Isolation Forest; reachability and SLA checks
3 Confirm over time
3 of 4 bad samples; 6 of 8 for latency-only alarms
Notes: 45 seconds: We validate telemetry before learning a healthy reference. Median and MAD produce a robust deviation score. Isolation Forest adds a statistical opinion for ordinary resource anomalies. Explicit reachability and individual flow service checks catch failures that statistical thresholds can miss. Temporal voting prevents a single noisy observation from becoming a persistent alarm. Detection describes the symptom, and diagnosis explains the likely cause.
Technical detail: each tick advances 0.5 modeled seconds. Initial readiness needs 60 consecutive trusted samples for the required observed entities. The robust score is z = (x − median) / max(1.4826 × MAD, metric floor). Ordinary resource alerts require z > 6, Isolation Forest agreement and debounce. Most raises need 3 bad votes among 4 samples. Latency-only raises need 6 among 8. Clearing needs 6 consecutive normal observations. Later route changes can relearn selected resource references from 20 trusted samples while retaining service and hard-reachability checks. Initial learning produces no active statistical alerts and must appear as learning or unknown. An unknown fault that passes admission checks can still contaminate the reference. Optional LSTM-AE inference adds sequence evidence. The saved five-second forecaster uses its original broader training label: loss above 2% or latency above twice baseline.
Sources: contracts/models.py, services/detector/detector.py, services/ml/forecast.py and services/ml/lstm_ae.py. Isolation Forest paper: https://cs.nju.edu.cn/zhouzh/zhouzh.files/publication/icdm08b.pdf

## Slide 3
NETHEAL / NC-04
Root cause analysis
Resource evidence plus the paths of failing traffic
03
Signature
Down link, loss while up, congestion, CPU or flapping
Path voting
Which component lies on the failing flows’ routes?
Supported cause
Show evidence; keep ambiguous symptoms uncertain
Notes: 45 seconds: A failing flow tells us where service suffers. We match resource signatures and identify components on the paths of failing flows. A down link carrying failing traffic supports link failure. Optional GraphSAGE inference helps rank candidates. The controller still requires observed support before considering a repair. We show the evidence and a reason for uncertainty when observations do not explain the current symptoms.
The rules-only rank is 0.6 × signature + 0.4 × path vote. With the GNN, it is 0.45 × signature + 0.25 × vote + 0.30 × GNN score. These are heuristic ranks. For example, signature 0.9 and three of four failing flows traversing a component give vote 0.75 and rules rank 0.84. This value is not a calibrated probability. Flapping uses a 20-tick history and at least two up/down transitions. Loss of at least 1% on an up link supports gray failure. Utilization of at least 0.8 supports congestion. A node CPU anomaly supports overload. An unreachable flow with observed healthy resources along its route can support forwarding misconfiguration. The healer requires the supported flag and a rank of at least 0.7.
Sources: services/rca/engine.py, services/ml/gnn.py, services/ml/graph.py and services/healer/healer.py. Path-voting inspiration, 007: https://www.usenix.org/conference/nsdi18/presentation/arzani . GraphSAGE: https://arxiv.org/abs/1706.02216 . The project uses a simplified rule and does not reproduce those papers' production results.

## Slide 4
NETHEAL / NC-04
Guarded repair and verification
A proposed route must restore service without harming others
04
Plan and test
A copied network, current evidence and policy limits
Apply under autonomy
Fresh approval when required; explicit failure outcomes
Measure every flow
Loss <1% · latency ≤1.1× baseline · load ≤85%
Notes: 20 to 30 seconds: The planner tests candidate repairs on a copied network. Capacity-aware joint routes and optional PPO proposals pass the same twin and policy checks. Autonomy determines whether a human must approve. Approval checks its deadline, generation, current state, evidence and a fresh prediction. We apply a permitted change and measure every affected and collateral flow. Execution or rollback failure has an explicit outcome. Later relapse clears current recovery status and permits one bounded recovery replan before escalation.
The twin predicts six ticks, equal to three modeled seconds. Observed verification also uses six ticks. Every flow needs valid reachable evidence on every sample, mean loss below 1%, and mean latency at most 1.1 times its frozen healthy baseline. Carrying-link utilization must stay at most 85% on every sample. The legacy aggregate substitutes 1,000 ms for unreachable traffic as a scoring sentinel. Per-flow reachability distinguishes that sentinel from a measured delay. L0 alerts, L1 recommends, L2 requires approval for every action, L3 automates at most one moved flow with risk at most 0.6, and L4 automates permitted actions. A bounded 32-state beam contributes at most three extra route combinations. It does not guarantee a globally optimal allocation. A three-second verification cannot guarantee a route will remain healthy throughout a longer fault ramp.
Sources: services/healer/healer.py, services/healer/incidents.py, config/healing.rego, services/policy.py and contracts/models.py. PPO algorithm reference: https://arxiv.org/abs/1707.06347 . The saved policy proposes constrained candidates. Its isolated training scores use a different task from operational recovery.

## Slide 5
NETHEAL / NC-04
Evaluation design
Repeatable scenarios, fixed denominators and sustained recovery
05
300 nominal scenarios × 7 policies
100 separate scenarios with hidden delay mismatch
Same scenario seeds • original affected services • last 10 s healthy
Recovery counts + uncertainty + collateral effects + unknown diagnoses
Notes: 45 seconds: We compare seven policies on the same seeded scenarios using independent network copies. We freeze the original exposed flow population and the no-healing service-impact denominator before judging repairs. A short verified repair and sustained recovery answer different questions. Sustained recovery requires all monitored services to satisfy the strict SLA on every one of the final 20 samples, equal to ten modeled seconds. We also measure collateral breaches, relapse, rollback and escalation.
The policies are no_heal, deliberately unsafe reactive, guarded_reactive, native_shortest, twin, predictive_twin and rl. Native shortest-path failover waits for three observed hard-failure ticks and uses static base costs. It is a limited reference, not full OSPF or ECMP. The nominal suite contains 300 scenarios: 274 faults and 26 healthy controls. Of the faults, 148 harm service in the no-healing reference and form the recovery denominator. Each run lasts 60 modeled seconds after warm-up. The separate stress suite has 100 scenarios with observed Library/CS latency multiplied by 1.18 during seconds 3 to 13 and 30 to 40. The planning twin cannot see that disturbance. Its impact denominator differs, so nominal and stress percentages cannot establish a causal recovery drop. Recovery proportions have Wilson 95% intervals. Paired bootstrap comparisons resample whole scenarios 2,000 times with seed 917. MTTD and MTTR use modeled seconds and disclose successful-case denominators. Artifacts retain raw runs, source/model hashes and seeds.
Sources: services/evaluator/harness.py, docs/EVALUATION.md, docs/evaluation.json and docs/LIMITATIONS.md.

## Slide 6
NETHEAL / NC-04
Measured sustained recovery
148 originally affected scenarios · strict SLA throughout the final 10 s
06
Chart: 
| No heal | Reactive* | Guarded | Native | Twin | Predictive | RL
Recovered (%) | 2.03 | 73.65 | 68.92 | 12.16 | 68.92 | 68.92 | 71.62
4 extra recovered with RL, 8 relapses. Overlapping 95% intervals limit the conclusion.
* Reactive bypasses safety. Compare recovery with collateral harm and escalation.
Notes: Read exact counts and denominators from the saved benchmark. In this nominal suite, twin and predictive_twin each sustain recovery in 102 of 148 service-impacting fault scenarios. RL recovers 106 of 148, but records eight relapses after initially verified repair. Twin and predictive_twin record none. Recovery confidence intervals overlap, and these figures do not establish RL superiority. The unsafe reactive baseline bypasses safeguards, so its recovery percentage alone cannot establish safety. Native failover covers observed hard-link failures.
Data source: docs/evaluation.json, generated 2026-10-07T07:04:28.959446+00:00.
Exact summary: {
"no_heal": {
"scenarios": 300,
"faults": 274,
"healthy": 26,
"disturbance_controls": 0,
"detection": {
"precision": 1,
"recall": 1,
"f1": 1,
"false_positive_rate": 0,
"disturbance_control_detection_rate": null,
"median_mttd_s": 1.5,
"median_mttd_gradual_s": 2.2
},
"rca": {
"top1": 0.8431,
"top3": 0.8431,
"voting_007_top1": 0.0328,
"diagnosed_faults": 274,
"coverage": 1,
"top1_over_all_faults": 0.8431,
"top1_given_diagnosis": 0.8431
},
"healing": {
"sla_impacting_faults": 148,
"recovered_rate": 0.0203,
"recovered_rate_ci95": [
0.0069,
0.0579
],
"recovered_faults": 3,
"applied_faults": 0,
"verified_faults": 0,
"relapsed_faults": 0,
"collateral_breach_faults": 0,
"median_recovery_s": 29.5,
"healed_rate": 0,
"median_mttr_s": null,
"rollback_rate": null,
"escalated_rate": 0
},
"sla": {
"violation_s_total": 7647,
"median_violation_s": 60,
"p95_latency_ms": 107.8,
"median_run_p95_latency_ms": 107.8,
"flow_violation_s_total": 14051.5,
"collateral_violation_s_after_action": 0,
"mean_loss_pct": 6.545
}
},
"reactive": {
"scenarios": 300,
"faults": 274,
"healthy": 26,
"disturbance_controls": 0,
"detection": {
"precision": 1,
"recall": 1,
"f1": 1,
"false_positive_rate": 0,
"disturbance_control_detection_rate": null,
"median_mttd_s": 1.5,
"median_mttd_gradual_s": 2.2
},
"rca": {
"top1": 0.8431,
"top3": 0.8431,
"voting_007_top1": 0.0328,
"diagnosed_faults": 274,
"coverage": 1,
"top1_over_all_faults": 0.8431,
"top1_given_diagnosis": 0.8431
},
"healing": {
"sla_impacting_faults": 148,
"recovered_rate": 0.7365,
"recovered_rate_ci95": [
0.6602,
0.8008
],
"recovered_faults": 109,
"applied_faults": 106,
"verified_faults": 106,
"relapsed_faults": 0,
"collateral_breach_faults": 0,
"median_recovery_s": 1.5,
"healed_rate": 0.7162,
"median_mttr_s": 4.5,
"rollback_rate": 0,
"escalated_rate": 0.2365
},
"sla": {
"violation_s_total": 2085.5,
"median_violation_s": 1.5,
"p95_latency_ms": 10.2,
"median_run_p95_latency_ms": 10.2,
"flow_violation_s_total": 2913,
"collateral_violation_s_after_action": 0,
"mean_loss_pct": 0.327
}
},
"guarded_reactive": {
"scenarios": 300,
"faults": 274,
"healthy": 26,
"disturbance_controls": 0,
"detection": {
"precision": 1,
"recall": 1,
"f1": 1,
"false_positive_rate": 0,
"disturbance_control_detection_rate": null,
"median_mttd_s": 1.5,
"median_mttd_gradual_s": 2.2
},
"rca": {
"top1": 0.8431,
"top3": 0.8431,
"voting_007_top1": 0.0328,
"diagnosed_faults": 274,
"coverage": 1,
"top1_over_all_faults": 0.8431,
"top1_given_diagnosis": 0.8431
},
"healing": {
"sla_impacting_faults": 148,
"recovered_rate": 0.6892,
"recovered_rate_ci95": [
0.6106,
0.7582
],
"recovered_faults": 102,
"applied_faults": 99,
"verified_faults": 99,
"relapsed_faults": 0,
"collateral_breach_faults": 0,
"median_recovery_s": 1.5,
"healed_rate": 0.6689,
"median_mttr_s": 4.5,
"rollback_rate": 0,
"escalated_rate": 0.2838
},
"sla": {
"violation_s_total": 2291,
"median_violation_s": 1.5,
"p95_latency_ms": 10.2,
"median_run_p95_latency_ms": 10.2,
"flow_violation_s_total": 4417,
"collateral_violation_s_after_action": 0,
"mean_loss_pct": 1.182
}
},
"native_shortest": {
"scenarios": 300,
"faults": 274,
"healthy": 26,
"disturbance_controls": 0,
"detection": {
"precision": 1,
"recall": 1,
"f1": 1,
"false_positive_rate": 0,
"disturbance_control_detection_rate": null,
"median_mttd_s": 1.5,
"median_mttd_gradual_s": 2.2
},
"rca": {
"top1": 0.8431,
"top3": 0.8431,
"voting_007_top1": 0.0328,
"diagnosed_faults": 274,
"coverage": 1,
"top1_over_all_faults": 0.8431,
"top1_given_diagnosis": 0.8431
},
"healing": {
"sla_impacting_faults": 148,
"recovered_rate": 0.1216,
"recovered_rate_ci95": [
0.0783,
0.1841
],
"recovered_faults": 18,
"applied_faults": 27,
"verified_faults": 0,
"relapsed_faults": 0,
"collateral_breach_faults": 0,
"median_recovery_s": 1.5,
"healed_rate": 0,
"median_mttr_s": null,
"rollback_rate": 0,
"escalated_rate": 0
},
"sla": {
"violation_s_total": 6685.5,
"median_violation_s": 58,
"p95_latency_ms": 15.7,
"median_run_p95_latency_ms": 15.7,
"flow_violation_s_total": 12140.5,
"collateral_violation_s_after_action": 0,
"mean_loss_pct": 4.155
}
},
"twin": {
"scenarios": 300,
"faults": 274,
"healthy": 26,
"disturbance_controls": 0,
"detection": {
"precision": 1,
"recall": 1,
"f1": 1,
"false_positive_rate": 0,
"disturbance_control_detection_rate": null,
"median_mttd_s": 1.5,
"median_mttd_gradual_s": 2.2
},
"rca": {
"top1": 0.8431,
"top3": 0.8431,
"voting_007_top1": 0.0328,
"diagnosed_faults": 274,
"coverage": 1,
"top1_over_all_faults": 0.8431,
"top1_given_diagnosis": 0.8431
},
"healing": {
"sla_impacting_faults": 148,
"recovered_rate": 0.6892,
"recovered_rate_ci95": [
0.6106,
0.7582
],
"recovered_faults": 102,
"applied_faults": 99,
"verified_faults": 99,
"relapsed_faults": 0,
"collateral_breach_faults": 0,
"median_recovery_s": 1.5,
"healed_rate": 0.6689,
"median_mttr_s": 4.5,
"rollback_rate": 0,
"escalated_rate": 0.2838
},
"sla": {
"violation_s_total": 2268,
"median_violation_s": 1.5,
"p95_latency_ms": 10.2,
"median_run_p95_latency_ms": 10.2,
"flow_violation_s_total": 4380,
"collateral_violation_s_after_action": 0,
"mean_loss_pct": 1.182
}
},
"predictive_twin": {
"scenarios": 300,
"faults": 274,
"healthy": 26,
"disturbance_controls": 0,
"detection": {
"precision": 1,
"recall": 1,
"f1": 1,
"false_positive_rate": 0,
"disturbance_control_detection_rate": null,
"median_mttd_s": 1.5,
"median_mttd_gradual_s": 1.5
},
"rca": {
"top1": 0.8431,
"top3": 0.8431,
"voting_007_top1": 0.0328,
"diagnosed_faults": 274,
"coverage": 1,
"top1_over_all_faults": 0.8431,
"top1_given_diagnosis": 0.8431
},
"healing": {
"sla_impacting_faults": 148,
"recovered_rate": 0.6892,
"recovered_rate_ci95": [
0.6106,
0.7582
],
"recovered_faults": 102,
"applied_faults": 99,
"verified_faults": 99,
"relapsed_faults": 0,
"collateral_breach_faults": 0,
"median_recovery_s": 1.5,
"healed_rate": 0.6689,
"median_mttr_s": 4.5,
"rollback_rate": 0,
"escalated_rate": 0.2838
},
"sla": {
"violation_s_total": 2268,
"median_violation_s": 1.5,
"p95_latency_ms": 10.2,
"median_run_p95_latency_ms": 10.2,
"flow_violation_s_total": 4380,
"collateral_violation_s_after_action": 0,
"mean_loss_pct": 1.182
}
},
"rl": {
"scenarios": 300,
"faults": 274,
"healthy": 26,
"disturbance_controls": 0,
"detection": {
"precision": 1,
"recall": 1,
"f1": 1,
"false_positive_rate": 0,
"disturbance_control_detection_rate": null,
"median_mttd_s": 1.5,
"median_mttd_gradual_s": 1.5
},
"rca": {
"top1": 0.8431,
"top3": 0.8431,
"voting_007_top1": 0.0328,
"diagnosed_faults": 274,
"coverage": 1,
"top1_over_all_faults": 0.8431,
"top1_given_diagnosis": 0.8431
},
"healing": {
"sla_impacting_faults": 148,
"recovered_rate": 0.7162,
"recovered_rate_ci95": [
0.6388,
0.7827
],
"recovered_faults": 106,
"applied_faults": 113,
"verified_faults": 113,
"relapsed_faults": 8,
"collateral_breach_faults": 0,
"median_recovery_s": 1.5,
"healed_rate": 0.7635,
"median_mttr_s": 4.5,
"rollback_rate": 0,
"escalated_rate": 0.2365
},
"sla": {
"violation_s_total": 1990.5,
"median_violation_s": 1.5,
"p95_latency_ms": 10.2,
"median_run_p95_latency_ms": 10.2,
"flow_violation_s_total": 3986,
"collateral_violation_s_after_action": 0,
"mean_loss_pct": 1.182
}
}
}
Confidence and provenance definitions are in metadata. The denominator consists of faults that harm service in the original no-healing reference. Sustained recovery requires the fixed monitored services to pass every sample in the final ten modeled seconds. The artifact establishes performance for this simulated population.

## Slide 7
NETHEAL / NC-04
When the twin misses delay
Stress experiment with a separate service-impact cohort
07
Stress outcome | No heal | Twin | RL
Sustained recovered | 36/92 | 53/92 | 54/92
Short verified | 0/92 | 17/92 | 18/92
Relapsed | 0/92 | 7/92 | 8/92
Rollback events | 0 | 50 | 51
Hidden observed delay, separate cohort.
Rollback cannot guarantee sustained recovery.
Notes: This separate experiment adds 18% observed Library/CS latency during seconds 3 to 13 and 30 to 40. The copied planning twin does not receive that disturbance. Ninety-two fault scenarios form this suite's service-impact denominator. Eight additional disturbance-only controls are separate from the fault table and are not healthy false-positive controls.
Sustained recovered, short verified and relapsed rows count scenarios. Short verified means at least one attempt passed its six-sample verification. Final recovery requires every sample in the final twenty-sample service window to pass, and can also occur after the disturbance ends. Rollback events count individual rollback outcomes across service-impacting fault runs. Some scenarios roll back more than once. Scenarios with any rollback: No heal 0, Twin 34, RL 35. Exact editable table: [["Stress outcome","No heal","Twin","RL"],["Sustained recovered","36/92","53/92","54/92"],["Short verified","0/92","17/92","18/92"],["Relapsed","0/92","7/92","8/92"],["Rollback events","0","50","51"]].
The table shows why an observed verification failure and attempted rollback do not guarantee sustained recovery. The observed post-action collateral breaches are associations under the injected disturbance, not proof that the action caused every breach. This stress cohort has a different impact denominator from the nominal suite, so directly comparing its recovery percentage with nominal recovery cannot establish a causal drop.
Source: docs/evaluation.json, stress.summary and stress.runs. Model: services/evaluator/harness.py. Scope: docs/LIMITATIONS.md.

## Slide 8
NETHEAL / NC-04
Scope and next validation
A tested simulation with visible limits
08
Demonstrated
Detection → supported diagnosis → guarded repair → evidence
Bounded claims
One campus model; heuristic scores; shared nominal physics
LLM boundary
Read-only explanation and reporting; offline templates
Notes: Closing, 15 seconds: The demonstration establishes the complete control loop and measurable recovery in a simulated campus. Production hardware, wider topologies and independently modeled physics require further validation. The LLM explains stored evidence and cannot apply routes.
For questions about the models, explain their separate tasks and the deterministic execution guards. Ordinary routing can reconverge after a hard link failure. Gray loss, overload or congestion may leave connectivity intact while service deteriorates. Planning uses bounded candidates on this campus and provides no proof of global optimality. When the twin is wrong, observed verification, rollback attempts and escalation reveal the failure. They cannot guarantee successful rollback in every case. Confidence values are heuristic ranks. Historical PPO experiments with oracle fault locations use a different task from the operational benchmark.
The nominal twin shares the simulator's equations. The separate stress suite challenges one bounded form of observation mismatch on the same topology. The eight nominal RL relapses occur during gradual overload ramps, illustrating why short verification and sustained recovery must be reported separately. Saved training weights were preserved, and their complete original lineage has not been independently reconstructed. Claim actual Docker, Mininet, Open vSwitch or live provider availability only after verifying those runtimes.
Sources: docs/LIMITATIONS.md, services/copilot/agent.py, services/llm/reports.py and services/evaluator/harness.py.